# Layers Reference
## Layers Definitions
Table C3: Device, LVS and other CAD definitions
Name	Defining algorithm			Used in …
AR_met2_A	Net Area Ratio of met2 not connected to via and of via2 >=0.05 [Equation: (AREA(via2))/(2 * AREA(met2NotConnVia) + PERIMETER(met2NotConnVia) * 0.35)]			Rules
AR_met2_B	Net Area Ratio of met2GroundOrFloat, via, and via2 <=0.032 [Equation: (AREA(via2))/(2 * AREA(met2GroundOrFloatVia) + PERIMETER(met2GroundOrFloatVia) * 0.35)]			Rules
bondPad	pad:dg OUTSIDE areaid:ft			Rules
bottom_plate	(capm:dg AND met2:dg) sized by capm.3; Exclude all capm sharing same metal2 plate			Rules
Capacitor	Capm enclosing at least one via2			Rules
Chip_extent	Holes (areaid:sl ) OR areaid.sl			Rules
Diecut_pmm	areaid.dt NOT (cfom.wp OR cp1m.wp OR cmm1.wp OR cmm2.wp)			Rules
drain_diffusion	(diff NOT poly in nwell or pwell) not abutting tap in the same well or abutting tap in the opposite well			Rules
dummy_capacitor	Capm not overlapping via2			Rules
dummy_poly	poly overlapping text “dummy_poly” (written using text.dg)			Rules
ESD_nwell_tap	n+ tap coincident with nwell such that n+ tap and nwell are completely surrounded by and abutting n+ diff on all edges, within areaid:ed			Rules
fomDmy_keepout_1	(diff.dg OR tap.dg OR poly.dg OR pwell resistor OR pad OR cfom.dg OR cfom.mk OR PhotoArray OR cp1m.mk)			Rules
floating_met*	met*.dg not connected to diffusion or tap through met(+1) or met(-1) and their respecitve vias and contacts			Rules
fom_waffles	fom.mk with dimensions (um x um): 0.5 x 0.5, 1.5 x 1.5, 2.5 x 2.5 and 4.08 x 4.08			Rules
gated_npn	cell name: s8rf_npn_1x1_2p0_HV			Rules
huge_metX	Metal X geometry wider and longer than 3.000um			Rules
hugePad	pad.mk with width > 100um			Rules
iso_pwell	(NOT nwell) AND dnwell			Rules
isolated_tap	tap that does not abut diff			Rules
laser_target	cell lazX_ and lazY_ OUTSIDE areaid:ft			Rules
LVnwell	nwell NOT hvi			Rules
LVTN_Gate	Gate overlapping lvtn			Rules
met2GroundOrFloat	met2 connected to ptap or met2 not connected to difftapn			Rules
met2GroundOrFloatVia	met2GroundOrFloat interacting with via2 >2			Rules
N+_diff	Diff NOT Nwell			Rules
N+_tap	Tap AND Nwell			Rules
nsdmHoles	Hole( nsdm )			Rules
NSM_keepout	nsm.dg OR nsm.mk			Rules
nwell_all	nwell OR extension of cnwm beyond nwell edge straddling de_nFet_source by cnwm.3f (45 degree edges are retained for the NVHV device nwell); Rule cnwm.3f applies only to GSMC flows			Rules
P+_diff	Diff AND Nwell			Rules
P+_tap	Tap NOT Nwell			Rules
Pattern_density	(diff_tap area) / PD window (as specified in the rule section)			Rules
photoDiode	deep nwell overlapping areaid.po. Die+frame utility will use the mask data of dnwell in the implementation of this definition			Rules
poly_licon1	Any licon1 that does not overlap ((diff or tap) NOT poly)			Rules
poly_waffles	p1m.mk with dimensions (um x um): 0.48 x 0.48, 0.54 x 0.54 and 0.72 x 0.72			Rules
prec_resistor	rpm AND (poly overlapping poly.rs) AND psdm			Rules
prec_resistor_terminal	prec_resistor AND li			Rules
psdmHoles	Hole( psdm )			Rules
pwell	NOT nwell (default substrate area)			Rules
pwres_terminal	P+tap abutting pwell.rs			Rules
pnp_emitter	diff AND pnp.dg AND psdm			Rules
routing_terminal	metX.pin sized inside of metX.drawing by 1/2 * metalX min width; Similar defintion applies to Li1 layer			Rules
scribe_line	areaid:ft NOT areaid:dt			Rules
slotted_licon	licon1.dg of size 0.19um x 2.0um			Rules
slotted_licon_edge1	2.0um edge of the slotted_licon			Rules
source_diffusion	(diff NOT poly in nwell or pwell) abutting tap in same well			Rules
tap_licon	Tap AND Licon1			Rules
tap_notPoly	tap NOT poly			Rules
top_indmMetal	met3 for S8D*			Rules
top_metal	met3.dg OR mm3.mk (for S8T*/SP8TEE-5R); met3.dg OR indm.mk (for S8D*); met4.dg OR mm4.mk (for SP8Q/S8Q*); met5.dg OR mm5.mk (for SP8P*/S8P*)			Rules
top_padVia	Via2 for S8D*			Rules
top_plate	capm:dg			Rules
Var_channel	poly AND tap AND (nwell NOT hvi) NOT areaid.ce			Rules
VaracTap	Tap overlapping Var_channel			Rules
vpp_with_noLi	vpp with cell names: FIXME			Rules
vpp_with_Met3Shield	vpp with cell names: FIXME			Rules
vpp_with_LiShield	vpp with cell names: FIXME			Rules
vpp_over_MOSCAP	vpp with cell names: FIXME when over nhvnative W/L=10x4, FIXME when over phv/pshort/phighvt/plowvt W/L=5x4			Rules
vpp_with_Met5PolyShield	vpp with cell names: FIXME			Rules
vpp_with_Met5	vpp with cell names: FIXME			Rules
cp1m_HV	cp1m AND Hvi			Rules (HV)
de_nFet_drain	((isolated tap) AND areaid.en) overlapping nwell			Rules (HV)
de_nFET_gate	deFET_gate overlapping (diff NOT dnwell)			Rules (HV)
de_nFet_source	(diff AND areaid.en) overlapping de_nFET_gate			Rules (HV)
de_pFet_drain	((isolated tap) AND areaid.en) not overlapping nwell			Rules (HV)
de_pFET_gate	deFET_gate overlapping (diff AND dnwell)			Rules (HV)
de_pFet_source	(diff AND areaid.en) overlapping de_pFET_gate			Rules (HV)
deFET_gate	(poly AND areaid.en) not overlapping pwm ; For CAD flows that do not have pwm layer, it is (poly AND areaid.en)			Rules (HV)
Hdiff	Diffusion AND Hvi			Rules (HV)
Hgate	Hpoly AND diff			Rules (HV)
Hnwell	Nwell AND Hvi			Rules (HV)
Hpoly	Poly AND Hvi			Rules (HV)
Htap	Tap AND Hvi			Rules (HV)
hv_source/drain	= (diff andNot poly) that overlaps diff.hv			Rules (HV)
hvFET_gate	= FET_gate butting hv_source/drain			Rules (HV)
hvPoly	= poly electrically connected to hv_source/drain			Rules (HV)
HV_nwell	(nwell AND hvi) OR (nwell overlapping areaid.hl)			Rules (HV)
stack_hv_lv_diff	(diff And Hvi NOT nwell) abutting (diff NOT nwell)			Rules (HV)
SHVdiff	Diff And shvi			Rules (SHV)
SHVGate	SHVPoly AND diff			Rules (SHV)
SHVPoly	Poly OVERLAP shvi:dg			Rules (SHV)
SHVSourceDrain	Diff And shvi NOT poly NOT diff:rs			Rules (SHV)
VHVdiff	Diff And vhvi			Rules (VHV)
VHVGate	VHVPoly AND diff			Rules (VHV)
VHVPoly	Poly OVERLAP vhvi:dg			Rules (VHV)
VHVSourceDrain	(Diff AND tap) And vhvi NOT poly NOT diff:rs			Rules (VHV)
background	Area where waffling grid is defined, sized to avoid waffle shift between runs			Waffles
die	Holes (areaid:sl )			Waffles
frame	( areaid.ft SIZE by -(max of s.2e/h)) NOT (OR areaid.dt SEALIDandHole)			Waffles
inductor_metal	(inductor:dg AND (met1 OR met2 OR met3)) size by 10 um [For all flows except S8PIR-10R]ninductor.dg [for the S8PIR-10R flow]			Waffles
mm*_slot	mm* slots are defined as empty holes in metal that are located in (areaid.cr OR areaid.cd)			Waffles
nwellDnwellHoles	(inner HOLES of nwellAndDnwell). Die+frame utility will use the mask data of nwell and dnwell in the implementation of this definition			Waffles
photoArray	(OR nwellAndDnwell nwellDnwellHoles) enclosing photoDiode. Die+frame utility will use the mask data of nwell and dnwell in the implementation of this definition			Waffles
gate	poly AND diff			pfet, nfet (LVS)
nfet	Gate NOT nwell			pfet, nfet (LVS)
pfet	Gate AND nwell			pfet, nfet (LVS)
nDiode	Ndiff AND DiodeID			Diodes (LVS)
Pdiff	diff AND nwell			Diodes (LVS)
pDiode	Pdiff AND DiodeID			Diodes (LVS)
diff_hole	Hole( diff )			ESD (LVS)
diff_tap_nwell	tap_nwell INSIDE diff_hole			ESD (LVS)
esd_diff_tap_nwell	ESDID AND diff_tap_nwell			ESD (LVS)
Ndiff	diff NOT nwell			ESD (LVS)
tap_nwell	tap INSIDE nwell			ESD (LVS)
ESD_diffusion	A+B31ny diffusion or ESD_nwell_tap connected directly or through a resistor to a Pad or to Vss/Vcc that is covered by areaid.ed and located within a double tap guardrings.			Latch up rules
ESD_cascode_diffusion	Diffusion covered by areaid.ed between two minimum spaced poly gates and located within a pair of double tap guardrings. (There should be no licons on the diffusion.)			Latch up rules
ESD_diode	Any nwell (other than ESD_nwell_tap ) covered by areaid.ed and areaid.de that does not contain poly			Latch up rules
ESD_FET	(any Pdiff covered by areaid:ed within a double tap guardrings) OrnESD_NFET			Latch up rules
ESD_NFET	(any Ndiff covered by areaid:ed abutting ESD_nwell_tap) Or (any Ndiff covered by areaid:ed abutting gate within 3.5um of ESD_nwell_tap) Or (any Ndiff abutting ESD_nwell_tap within areaid.ed) a double tap guardrings			Latch up rules
I/O_or_Output_Pmos	ESD P+ diffusion overlapping poly and overlapping ESD source/drain diffusion connected to I/O or output net			Latch up rules
I/O_Pmos_w/series_R	ESD PMOS connected to I/O or output net through series resistors			Latch up rules
met_ESD_resistor	Metal resistor inside areaid:ed			Latch up rules
Non_Vcc_nwell	Any nwell connected to any bias other than power supply			Latch up rules
Nwell_area	Is determined using the following steps:n(a) Grow pdiff by 1.5 mmn(b) Mergen(c) And Nwell:dg			Latch up rules
Pwell_area	Is determined using the following steps:n(a) Grow ndiff by 1.5 mmn(b) Mergen(c) NOT Nwell:dg			Latch up rules
Series_transistors	Merged diffusion determined by Nwell_area and Pwell_area			Latch up rules
fuse:dg	met2:fe for S8D*/S8TM*, met3.fe for S8TEE*/S8TNV/S8Q*/SP8TEE-5R/SP8Q*, met4.fe for S8P*/SP8P*			Fuse rules
fuse_contact	(fuse_metal overlapping fuse:dg) NOT fuse:dg			Fuse rules
fuse_metal	met3 for S8TEE*/S8TNV/S8Q*/SP8TEE-5R/SP8Q*; met2 for S8D*/S8TM*, met4 for S8P*/SP8P*			Fuse rules
fuse_shield	Metal line (same metal level as fuse) between fuse and periphery, not overlapping contacts or vias, with specified dimensions			Fuse rules
non-isolated fuse edge	Long edge of the fuse spaced to Met2/Met3/Met4 less than a specified amount			Fuse rules
single_fuses	Fuses without neighboring fuses within specified distance			Fuse rules

## Auxiliary Layers
Table C4a: Purpose layer description in LSW window and Auxiliary Layers
waffle_chip		icfb ver 5.0			icfb ver 5.1
drawing		dg			drw
pin		pn			pin
boundary		by			bnd
net		nt			net
res		rs			res
label		ll			lbl
cut		ct			cut
short		st			sho
pin		pn			pin
gate		ge			gat
probe		pe			pro
blockage		be			blo
model		ml			mod
optionX (X = 1…n)		oX (X = 1..n)			opt*(X=1..n)
fuse		fe			fus
mask		mk			mas*
maskAdd		md			mas*
maskDrop		mp			mas*
waffleAdd1		w1			waffleAdd1
waffleAdd2		w2			waffleAdd2
waffleDrop		wp			waf
error		er			err
warning		wg			wng
dummy		dy			dmy
Table C4b: Purpose layer description in LSW window and Auxiliary Layers¶
waffle_chip	icfb ver 5.0		icfb ver 5.1
drawing	dg		drw
pin	pn		pin
boundary	by		bnd
net	nt		net
res	rs		res
label	ll		lbl
cut	ct		cut
short	st		sho
pin	pn		pin
gate	ge		gat
probe	pe		pro
blockage	be		blo
model	ml		mod
optionX (X = 1…n)	oX (X = 1..n)		opt*(X=1..n)
fuse	fe		fus
mask	mk		mas*
maskAdd	md		mas*
maskDrop	mp		mas*
waffleAdd1	w1		waffleAdd1
waffleAdd2	w2		waffleAdd2
waffleDrop	wp		waf
error	er		err
warning	wg		wng
dummy	dy		dmy

Layout Data Name & GDSII No.	Brief description		icfb ver 5.1	Identifiesn(See WOLF-41, SPR 95111 for more details)		Who		Use
areaid.sl{81:1}	areaid sealring		areaid.sea	The area of the Seal ring		Tech
areaid.ww{81:13}	areaid Waffle Window		areaid.waf	Used to prevent waffle shifting. When larger than areaid:sl re-defines the placement of waffles.		Frame		CLDRC
areaid.dn{81:50}	areaid dead Zon		areaid.dea	“deadzone” area in the DieSealR pcell (Seal Ring) for metal stress relief rule checks		Tech
areaid.cr{81:51}	areaid critCorner		areaid.cri*	For portions of layout that are not to be put in the critical side do to stress constraints. Should be used sparingly and only over the portion of the layout to remove DRC violations. Avoid using a blanket polygon over the entire layout. This layer is to be used instead of using the noCritSideReg verification option in Stress.n“critical corner” area in the DieSealR pcell (Seal Ring) for metal stress relief rule checks		Tech		Stress
areaid.cd{81:52}	areaid critSid		areaid.cri*	“criticalsid” area in the DieSealR pcell (Seal Ring) for metal stress relief rule checks		Tech		Stress
areaid.ce{81:2}	areaid core		areaid.cor	Memory core (memory cells and approved on-pitch only)		Tech		DRC
areaid.fe{81:3}	areaid frame		areaid.fra*	Pads in the frame		Frame		DRC
areaid.ed{81:19}	areaid ESD		areaid.esd	ESD devices- Surrounds any diffusion or ESD nwell tap connected to a signal pad. (only over ESD devices with special poly/tap exemption rules per LFL)		ESD, Des		DRC
areaid.dt{81:11}	areaid die cut		areaid.die	Location of the die within the frame used in frame builder ngeneration to create blanking for die and other drop-ins. Also used in cldrc/drc for rules in frame to die edge (waffles, nsm, metals etc)		Frame		Tech
areaid.mt{81:10}	areaid module cut		areaid.mod	Location of e-test modules within the frame used in frame builder generation to create data in scribe lane(example: opaque/clear masks) and to mark location of cells (etest and fab)for frame reports. Also used in drc/cldrc for rules to cell edge.		Frame		Tech
areaid.ft{81:12}	areaid frameRect		areaid.fra*	Boundary of the frame used in frame builder generation to mark boundary of frame. Also used in cldrc/drc for rules to frame edge		Frame		DRC/CLDRC
areaid.de{81:23}	areaid Diode		areaid.dio	The area occupied by diodes; Used to identify diodes during LVS		All		LVS
areaid.sc{81:4}	areaid standardc		areaid.sta	Cells in the standard cell library (over standard cell IP blocks only) .		Standard cell		DRC
areaid.st{81:53}	areaid SubstrateCut		areaid.sub	Regions to be considered as isolated substrates (only to designate 2 different resistively connected substrate nregions, >100um apart)		Tech, Des, ESD		Latch up, LVS, soft
areaid.en{81:57}	areaid extended drain		areaid.ext	Used to identify the extended drain devices		Tech, Des, ESD		LVS
areaid.le{81:60}	areaid LV Native		areaid.lvn	Used to identify the 3V Native NMOS versus 5V Native NMOS		Tech, Des		LVS
areaid.po{81:81}	areaid photo		areaid.pho	The areaid id is to identify the dnwell photo diode		Tech, Des		DRC
areaid.et{81:101}	areaid etest		areaid.ete	Used in etest modules		Frame		DRC
areaid.ld{81:14}	areaid low tap density		areaid.low	6um tap to diff rule will not be checked in this regionnDiffusion >6u from related tap, requiring >50u from sigPadDiff && sigPadMetNtr).nShould be used sparingly and only over the portion of the layout to remove DRC violations. This layer is not to be used if a tapping solution can be found. This layer can only be used if there is low risk for latchup. This layer will be reviewed during PDQC.		All		DRC
areaid.ns{81:15)	areaid not-crtical side		areaid .not	critSideReg stress rules will not be checked in this regionnCannot be placed in the critical side – uncommon, or where stress nerrors can’t be fixed)		All		DRC
areaid.ij{81:17}	areaid injection		areaid.inj	Identify all circuits that are susceptible to injection and ensure no signal-pad connected diffusion is within 100u.n“areaid.inj” encloses any circuitry deemed sensitive (by design team) to injected substrate areaid.inj encloses any PVT compliant circuitry		All		DRC
areaid.hl{81:63}	areaid.hvnwell		areaid.hvn	Identify nwell hooked to HV but containing FETs with thin oxide; nPotential difference across the FET terminals is LVnUsed over lv devices, operating in lv mode, placed in hv nwells, and should NOT have hvi		All		DRC
areaid.re{81:125}	areaid rf diode		areaid.rfd	Defines rf diodes that need to be extracted with series resistance (memo GCZ-124/125)		All		LVS
areaid.rd{81:24}	areaid.rdlprobepad		areaid.rdl	Ignore RDL keepouts when opening up PMM2		All		CLDRC
areaid.sf{81:6}	areaid sigPadDiff			Identify all srdrn diffusions and tap which are intended to be nconnected to signal pad (io Nets). Goes over diffusions connected to a signal pad - including through a poly resistor		All		LATCHUP
areaid.sl{81:7}	areaid.sigPadWell			Identify all nwells and pwells which are intended to be connected to signal pad (io Nets). Goes over wells with tap connected to a signal pad, including through a poly resistor		All		LATCHUP
areaid.sr{81:8}	areaid sigPadMetNtr			Identify all srcdrn, tap, and wells which are intended to be nmetallically connected to signal pad (io Nets) not through a resistor. nMust be used in unison with areaid.sigPadDifff or areaid.sigPadWell.nUsed with one of the above 2 areaids, nodes metallically nconnection to a sigPad (not through res)		All		LATCHUP
inductor:dg{82:24}	ID layer for inductor			Inductors		Tech, Des		DRC
t1,2,3 {82:26, 27, 28}	terminal labels for inductor			Labels required by inductor terminals to be recognized as device		Tech, Des		LVS
poly:ml {66:83}	poly device model			Model name extraction		Tech, Des, ESD		LVS
ncm {92:44}	N-Core Implant			Ncm.dg is available as a drawn layer		All		DRC/CLDRC
protect)	VPP capacitor			Interdigitated, vertical Li1, M1 and M2 capacitor		All		LVS
capm_2t.dg	MIM caps (2 terminal model)			ID layer for MIMCAP that will be treated as 2T device		All		DRC/LVS
cpmm:dg{91}	Drawn compatible polyimide layer			Drawn compatible layer and used only inside S8 RF pad		Frame
li1.be{67:10}	li1 blockage layer			Li1 blockage layer used for IP integration (per CWR 137)		All		DRC
met1.be{68:10}	Metal1 blockage layer			Metal 1 blockage layer used for IP integration (per CWR 137)		All		DRC
met2.be{69:10}	Metal2 blockage layer			Metal 2 blockage layer used for IP integration (per CWR 137)		All		DRC
met3.be{70:10}	Metal3 blockage layer			Metal 3 blockage layer used for IP integration (per CWR 137)		All		DRC
met4.be{71:10}	Metal4 blockage layer			Metal 4 blockage layer used for IP integration (per CWR 137)		All		DRC
met5.be{72:10}	Metal5 blockage layer			Metal 5 blockage layer used for IP integration (per CWR 137)		All		DRC
vhvi {74:21}	Very High voltage id layer			Used to identify nodes that operate at 12V nominal (16V max)		Des		VHV Rules
uhvi {74:22}	Ultra High voltage id layer			Used to identify nodes that operate at 20V nominal		Des		UHV Rules
areaid.e0{81:58}	Area extended drain		areaid.ext	Used to identify 20V drain extended devices		Des		LVS
areaid.zr{81:18}	Area zener diode		areaid.zen	Used to identify Zener diodes		Des		LVS
fom.dy{}	FOM dummy			FOM waffle drawn in this layer		All		Waffles
prune:dg{84:44}	prune			Areas ignored by LVS		Frame		LVS
areaid:cr {81:55}	copper pillar (.cuPillar)		areaid.cup	Placement of Cu pillar over the pad area, streamed out to Amkor, s8pfhd-10r flow only		Die		CLDRC s8pfhd-10r
cyprotect.dg {56.44}	External F25 layer		cyprotect.dg	Switch to direct streaming to drawn (no protect) or mask layer (with protect)		Frame		CLDRC
cytextmc.dg {50:44}	Locations for mask compose		cytextmc.dg	Text to extract placement for Fab25 tool		Frame		CLDRC
cypsbr.dg {51:44}	No phaseshift allowed		cypsbr.dg	Phaseshift layer common to all F25 phaseshift masks		Frame
areaid:ag{81:79}	analog		areaid.ana	Used to identify analog circuits		All		Analog
natfet.dg {124:21}	DEFETs		natfet.dg	Add TUNM for SONOS channel implants. See SPR 117559, SGL-529		All		DRC/CLDRC
areaid:lw	Ultra High voltage id layer			Areaid low voltage: UHV box to put all HV/LV curcuits in		All		Analog
To distinguish the layers, the full name of the layer needs to be turned on in the LSW window
As the layers are displayed in LSW window in icfb version 5.0; For purpose layer displayed in version 5.1, pls refer table C3

## Devices and Layout vs Schematic (LVS) Information
Table F2a: Devices and Layout vs. Schematic (LVS)
waffle_chip	icfb ver 5.0	icfb ver 5.1
drawing	dg	drw
pin	pn	pin
boundary	by	bnd
net	nt	net
res	rs	res
label	ll	lbl
cut	ct	cut
short	st	sho
pin	pn	pin
gate	ge	gat
probe	pe	pro
blockage	be	blo
model	ml	mod
optionX (X = 1…n)	oX (X = 1..n)	opt*(X=1..n)
fuse	fe	fus
mask	mk	mas*
maskAdd	md	mas*
maskDrop	mp	mas*
waffleAdd1	w1	waffleAdd1
waffleAdd2	w2	waffleAdd2
waffleDrop	wp	waf
error	er	err
warning	wg	wng
dummy	dy	dmy

Layout Data Name & GDSII No.	Brief description	icfb ver 5.1	Identifiesn(See WOLF-41, SPR 95111 for more details)	Who	Use
areaid.sl{81:1}	areaid sealring	areaid.sea	The area of the Seal ring	Tech
areaid.ww{81:13}	areaid Waffle Window	areaid.waf	Used to prevent waffle shifting. When larger than areaid:sl re-defines the placement of waffles.	Frame	CLDRC
areaid.dn{81:50}	areaid dead Zon	areaid.dea	“deadzone” area in the DieSealR pcell (Seal Ring) for metal stress relief rule checks	Tech
areaid.cr{81:51}	areaid critCorner	areaid.cri*	For portions of layout that are not to be put in the critical side do to stress constraints. Should be used sparingly and only over the portion of the layout to remove DRC violations. Avoid using a blanket polygon over the entire layout. This layer is to be used instead of using the noCritSideReg verification option in Stress.n“critical corner” area in the DieSealR pcell (Seal Ring) for metal stress relief rule checks	Tech	Stress
areaid.cd{81:52}	areaid critSid	areaid.cri*	“criticalsid” area in the DieSealR pcell (Seal Ring) for metal stress relief rule checks	Tech	Stress
areaid.ce{81:2}	areaid core	areaid.cor	Memory core (memory cells and approved on-pitch only)	Tech	DRC
areaid.fe{81:3}	areaid frame	areaid.fra*	Pads in the frame	Frame	DRC
areaid.ed{81:19}	areaid ESD	areaid.esd	ESD devices- Surrounds any diffusion or ESD nwell tap connected to a signal pad. (only over ESD devices with special poly/tap exemption rules per LFL)	ESD, Des	DRC
areaid.dt{81:11}	areaid die cut	areaid.die	Location of the die within the frame used in frame builder ngeneration to create blanking for die and other drop-ins. Also used in cldrc/drc for rules in frame to die edge (waffles, nsm, metals etc)	Frame	Tech
areaid.mt{81:10}	areaid module cut	areaid.mod	Location of e-test modules within the frame used in frame builder generation to create data in scribe lane(example: opaque/clear masks) and to mark location of cells (etest and fab)for frame reports. Also used in drc/cldrc for rules to cell edge.	Frame	Tech
areaid.ft{81:12}	areaid frameRect	areaid.fra*	Boundary of the frame used in frame builder generation to mark boundary of frame. Also used in cldrc/drc for rules to frame edge	Frame	DRC/CLDRC
areaid.de{81:23}	areaid Diode	areaid.dio	The area occupied by diodes; Used to identify diodes during LVS	All	LVS
areaid.sc{81:4}	areaid standardc	areaid.sta	Cells in the standard cell library (over standard cell IP blocks only) .	Standard cell	DRC
areaid.st{81:53}	areaid SubstrateCut	areaid.sub	Regions to be considered as isolated substrates (only to designate 2 different resistively connected substrate nregions, >100um apart)	Tech, Des, ESD	Latch up, LVS, soft
areaid.en{81:57}	areaid extended drain	areaid.ext	Used to identify the extended drain devices	Tech, Des, ESD	LVS
areaid.le{81:60}	areaid LV Native	areaid.lvn	Used to identify the 3V Native NMOS versus 5V Native NMOS	Tech, Des	LVS
areaid.po{81:81}	areaid photo	areaid.pho	The areaid id is to identify the dnwell photo diode	Tech, Des	DRC
areaid.et{81:101}	areaid etest	areaid.ete	Used in etest modules	Frame	DRC
areaid.ld{81:14}	areaid low tap density	areaid.low	6um tap to diff rule will not be checked in this regionnDiffusion >6u from related tap, requiring >50u from sigPadDiff && sigPadMetNtr).nShould be used sparingly and only over the portion of the layout to remove DRC violations. This layer is not to be used if a tapping solution can be found. This layer can only be used if there is low risk for latchup. This layer will be reviewed during PDQC.	All	DRC
areaid.ns{81:15)	areaid not-crtical side	areaid .not	critSideReg stress rules will not be checked in this regionnCannot be placed in the critical side – uncommon, or where stress nerrors can’t be fixed)	All	DRC
areaid.ij{81:17}	areaid injection	areaid.inj	Identify all circuits that are susceptible to injection and ensure no signal-pad connected diffusion is within 100u.n“areaid.inj” encloses any circuitry deemed sensitive (by design team) to injected substrate areaid.inj encloses any PVT compliant circuitry	All	DRC
areaid.hl{81:63}	areaid.hvnwell	areaid.hvn	Identify nwell hooked to HV but containing FETs with thin oxide; nPotential difference across the FET terminals is LVnUsed over lv devices, operating in lv mode, placed in hv nwells, and should NOT have hvi	All	DRC
areaid.re{81:125}	areaid rf diode	areaid.rfd	Defines rf diodes that need to be extracted with series resistance (memo GCZ-124/125)	All	LVS
areaid.rd{81:24}	areaid.rdlprobepad	areaid.rdl	Ignore RDL keepouts when opening up PMM2	All	CLDRC
areaid.sf{81:6}	areaid sigPadDiff		Identify all srdrn diffusions and tap which are intended to be nconnected to signal pad (io Nets). Goes over diffusions connected to a signal pad - including through a poly resistor	All	LATCHUP
areaid.sl{81:7}	areaid.sigPadWell		Identify all nwells and pwells which are intended to be connected to signal pad (io Nets). Goes over wells with tap connected to a signal pad, including through a poly resistor	All	LATCHUP
areaid.sr{81:8}	areaid sigPadMetNtr		Identify all srcdrn, tap, and wells which are intended to be nmetallically connected to signal pad (io Nets) not through a resistor. nMust be used in unison with areaid.sigPadDifff or areaid.sigPadWell.nUsed with one of the above 2 areaids, nodes metallically nconnection to a sigPad (not through res)	All	LATCHUP
inductor:dg{82:24}	ID layer for inductor		Inductors	Tech, Des	DRC
t1,2,3 {82:26, 27, 28}	terminal labels for inductor		Labels required by inductor terminals to be recognized as device	Tech, Des	LVS
poly:ml {66:83}	poly device model		Model name extraction	Tech, Des, ESD	LVS
ncm {92:44}	N-Core Implant		Ncm.dg is available as a drawn layer	All	DRC/CLDRC
protect)	VPP capacitor		Interdigitated, vertical Li1, M1 and M2 capacitor	All	LVS
capm_2t.dg	MIM caps (2 terminal model)		ID layer for MIMCAP that will be treated as 2T device	All	DRC/LVS
cpmm:dg{91}	Drawn compatible polyimide layer		Drawn compatible layer and used only inside S8 RF pad	Frame
li1.be{67:10}	li1 blockage layer		Li1 blockage layer used for IP integration (per CWR 137)	All	DRC
met1.be{68:10}	Metal1 blockage layer		Metal 1 blockage layer used for IP integration (per CWR 137)	All	DRC
met2.be{69:10}	Metal2 blockage layer		Metal 2 blockage layer used for IP integration (per CWR 137)	All	DRC
met3.be{70:10}	Metal3 blockage layer		Metal 3 blockage layer used for IP integration (per CWR 137)	All	DRC
met4.be{71:10}	Metal4 blockage layer		Metal 4 blockage layer used for IP integration (per CWR 137)	All	DRC
met5.be{72:10}	Metal5 blockage layer		Metal 5 blockage layer used for IP integration (per CWR 137)	All	DRC
vhvi {74:21}	Very High voltage id layer		Used to identify nodes that operate at 12V nominal (16V max)	Des	VHV Rules
uhvi {74:22}	Ultra High voltage id layer		Used to identify nodes that operate at 20V nominal	Des	UHV Rules
areaid.e0{81:58}	Area extended drain	areaid.ext	Used to identify 20V drain extended devices	Des	LVS
areaid.zr{81:18}	Area zener diode	areaid.zen	Used to identify Zener diodes	Des	LVS
fom.dy{}	FOM dummy		FOM waffle drawn in this layer	All	Waffles
prune:dg{84:44}	prune		Areas ignored by LVS	Frame	LVS
areaid:cr {81:55}	copper pillar (.cuPillar)	areaid.cup	Placement of Cu pillar over the pad area, streamed out to Amkor, s8pfhd-10r flow only	Die	CLDRC s8pfhd-10r
cyprotect.dg {56.44}	External F25 layer	cyprotect.dg	Switch to direct streaming to drawn (no protect) or mask layer (with protect)	Frame	CLDRC
cytextmc.dg {50:44}	Locations for mask compose	cytextmc.dg	Text to extract placement for Fab25 tool	Frame	CLDRC
cypsbr.dg {51:44}	No phaseshift allowed	cypsbr.dg	Phaseshift layer common to all F25 phaseshift masks	Frame
areaid:ag{81:79}	analog	areaid.ana	Used to identify analog circuits	All	Analog
natfet.dg {124:21}	DEFETs	natfet.dg	Add TUNM for SONOS channel implants. See SPR 117559, SGL-529	All	DRC/CLDRC
areaid:lw	Ultra High voltage id layer		Areaid low voltage: UHV box to put all HV/LV curcuits in	All	Analog
To distinguish the layers, the full name of the layer needs to be turned on in the LSW window
As the layers are displayed in LSW window in icfb version 5.0; For purpose layer displayed in version 5.1, pls refer table C3

Explanation of symbols: * - = Layer illegal for the device * + = Layer allowed to overlap * D = DRAWN indicates that a layer is drawn by Design. * C = CREATED indicates that the layer is only created by CAD.
Footnotes :
1
Low vt needs to be set on the schematic element
2
Ncm is drawn inside core. Otherwise it is created in periphery. See rules ncm.X.* for details
3(1,2,3,4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,19)
Drawn over half of device
4
ASSUMPTION: FET models will be same regardless of backend flow
5(1,2,3,4,5,6)
The 2 core FETs and flash npass must have a poly.ml label with their model name.
6(1,2,3,4,5,6,7)
over the drain
7(1,2,3,4,5,6,7)
over the source
8(1,2,3,4,5,6,7,8,9,10,11,12,13,14)
Information for RCX
9
Uses a black box for LVS. This is a fixed layout; Use symbol provided by modeling group
10
LVS will check that phighvt inside areaid.ce overlaps ncm
11(1,2,3)
The default model is sonos_e, sonos_de and nvssonos_e. If sonos_p, sonos_dp and nvssonos_p model are required, poly.ml must be used
12(1,2,3,4,5,6)
The capacitor.dg is drawn 0.17um from the edge of the cell to be LVS clean
13(1,2,3)
Devices are LVS’ed by cell name, m=1 per cell, fixed area and perimeter (see QHC-18)
14
(dnwell not (pwres or pnp or npn or areaid.en or areaid.de or areaid.po)) not nwell must have condiode text; Refer to VUN-104, 192 for condiode usage
15
Tech element is created by the user, no CAD supplied tech element
16(1,2,3)
There are multiple configurations of the Cu inductor. The layers present in one configuration may not be drawn in the other configuration. Also rdl will not be routed over met5 cu inductor, not checkable by CAD flow.
17(1,2,3,4)
Used for substrate noise isolation regions only
18(1,2)
Either UHVI or areaid.low_vt should be drawn over the sturctures
19(1,2)
Psub-Deep Nwell Diode must have condiode text “condiodeHvPsub”; CVA-596
20
mrp1 can’t overlay capacitor.dg: exempted s8rf2_xcmvpp11p5x11p7_lim5shield from the rule
## GDS Layers Information
The gds_layers.csv file provides a raw list of the layers used in the process with name, description and the GDS layer and data type.
Table - GDS Layers
Layer name	Purpose	GDS layer : datatype	Description
diff	drawing, text	65:20	Active (diffusion) area (type opposite of well/substrate underneath)
tap	drawing	65:44	Active (diffusion) area (type equal to the well/substrate underneath) (i.e., N+ and P+)
nwell	drawing	64:20	N-well region
dnwell	drawing	64:18	Deep n-well region
pwbm	drawing	19:44	Regions (in UHVI) blocked from p-well implant (DE MOS devices only)
pwde	drawing	124:20	Regions to receive p-well drain-extended implants
hvtr	drawing	18:20	High-Vt RF transistor implant
hvtp	drawing	78:44	High-Vt LVPMOS implant
ldntm	drawing	11:44	N-tip implant on SONOS devices
hvi	drawing	75:20	High voltage (5.0V) thick oxide gate regions
tunm	drawing	80:20	SONOS device tunnel implant
lvtn	drawing	125:44	Low-Vt NMOS device
poly	drawing, text	66:20	Polysilicon
hvntm	drawing	125:20	High voltage N-tip implant
nsdm	drawing	93:44	N+ source/drain implant
psdm	drawing	94:20	P+ source/drain implant
rpm	drawing	86:20	300 ohms/square polysilicon resistor implant
urpm	drawing	79:20	2000 ohms/square polysilicon resistor implant
npc	drawing	95:20	Nitride poly cut (under licon1 areas)
licon1	drawing	66:44	Contact to local interconnect
li1	drawing, text	67:20	Local interconnect
mcon	drawing	67:44	Contact from local interconnect to metal1
met1	drawing, text	68:20	Metal 1
via	drawing	68:44	Contact from metal 1 to metal 2
met2	drawing, text	69:20	Metal 2
via2	drawing	69:44	Contact from metal 2 to metal 3
met3	drawing, text	70:20	Metal 3
via3	drawing	70:44	Contact from metal 3 to metal 4
met4	drawing, text	71:20	Metal 4
via4	drawing	71:44	Contact from metal 4 to metal 5
met5	drawing, text	72:20	Metal 5
pad	drawing, text	76:20	Passivation cut (opening over pads)
nsm	drawing	61:20	Nitride seal mask
capm	drawing	89:44	MiM capacitor plate over metal 3
cap2m	drawing	97:44	MiM capacitor plate over metal 4
vhvi	drawing	74:21	12V nominal (16V max) node identifier
uhvi	drawing	74:22	20V nominal node identifier
npn	drawing	82:20	Base region identifier for NPN devices
inductor	drawing	82:24	Identifier for inductor regions
capacitor	drawing	82:64	Identifier for interdigitated (vertical parallel plate (vpp)) capacitors
pnp	drawing	82:44	Base nwell region identifier for PNP devices
LVS prune	drawing	84:44	Exemption from LVS check (used in e-test modules only)
ncm	drawing	92:44	N-core implant
padCenter	drawing	81:20	Pad center marker
target	drawing	76:44	Metal fuse target

areaid.sl	identifier	81:1	Seal ring identifier
areaid.ce	identifier	81:2	Memory (SRAM) core cell identifier
areaid.fe	identifier	81:3	Pads in padframe identifier
areaid.sc	identifier	81:4	Standard cell identifier
areaid.sf	identifier	81:6	Signal pad diffusion identifier (for latchup DRC checks)
areaid.sl	identifier	81:7	Signal pad well identifier (for latchup DRC checks)
areaid.sr	identifier	81:8	Signal pad metal (for latchup DRC checks)
areaid.mt	identifier	81:10	Location of e-test modules within the frame
areaid.dt	identifier	81:11	Location of dice within the frame
areaid.ft	identifier	81:12	Boundary of the frame
areaid.ww	identifier	81:13	Waffle window (used to prevent waffle shifting)
areaid.ld	identifier	81:14	Low tap density (15um between taps) area. Must be at least 50um from padframe
areaid.ns	identifier	81:15	Non-critical side. Blocks stress DRC rules
areaid.ij	identifier	81:17	Identification for areas susceptible to injection
areaid.zr	identifier	81:18	Zener diode identifier
areaid.ed	identifier	81:19	ESD device identifier
areaid.de	identifier	81:23	Diode identifier
areaid.rd	identifier	81:24	RDL probe pad (not used in this process)
areaid.dn	identifier	81:50	Dead zone (used in seal ring only for stress DRC)
areaid.cr	identifier	81:51	Critical corner (used in seal ring only for stress DRC)
areaid.cd	identifier	81:52	Critical side (used in seal ring only for stress DRC)
areaid.st	identifier	81:53	Substrate cut. Idendifies areas to be considered as isolated substrate
areaid.op	identifier	81:54	OPC drop. Block automatic OPC (for fab blocks and lithocal structures)
areaid.en	identifier	81:57	Extended drain identifier
areaid.en20	identifier	81:58	20V Extended drain identifier
areaid.le	identifier	81:60	3.3V native NMOS identifier (absence indicates a 5V native NMOS)
areaid.hl	identifier	81:63	HV nwell. Identifies nwells with thin oxide devices connected to high voltage
areaid.sd	identifier	81:70	subcircuit identifier (for LVS extraction)
areaid.po	identifier	81:81	Photodiode device identifier
areaid.it	identifier	81:84	IP exempt from DFM rules
areaid.et	identifier	81:101	e-test module identifier
areaid.lvt	identifier	81:108	Low-Vt identifier
areaid.re	identifier	81:125	RF diode identifier

fom	dummy	22:23

poly	gate	66:9

poly	model	66:83	(Text type)

poly	resistor	66:13
diff	resistor	65:13
pwell	resistor	64:13
li1	resistor	67:13

diff	high voltage	65:8

met4	fuse	71:17

inductor	terminal1	82:26
inductor	terminal2	82:27
inductor	terminal3	82:28

li1	block	67:10
met1	block	68:10
met2	block	69:10
met3	block	70:10
met4	block	71:10
met5	block	72:10

prBndry	boundary	235:4
diff	boundary	65:4
tap	boundary	65:60
mcon	boundary	67:60
poly	boundary	66:4
via	boundary	68:60
via2	boundary	69:60
via3	boundary	70:60
via4	boundary	71:60

li1	label	67:5	(Text type)
met1	label	68:5	(Text type)
met2	label	69:5	(Text type)
met3	label	70:5	(Text type)
met4	label	71:5	(Text type)
met5	label	72:5	(Text type)
poly	label	66:5	(Text type)
diff	label	65:6	(Text type)
pwell	label	64:59	(Text and data type)
pwelliso	label	44:5	(Text type)
pad	label	76:5	(Text type)
tap	label	65:5
nwell	label	64:5
inductor	label	82:25

text	label	83:44	(Text type)

li1	net	67:23	(Text type)
met1	net	68:23	(Text type)
met2	net	69:23	(Text type)
met3	net	70:23	(Text type)
met4	net	71:23	(Text type)
met5	net	72:23	(Text type)
poly	net	66:23	(Text type)
diff	net	65:23	(Text type)

li1	pin	67:16	(Text and data)
met1	pin	68:16	(Text and data)
met2	pin	69:16	(Text and data)
met3	pin	70:16	(Text and data)
met4	pin	71:16	(Text and data)
met5	pin	72:16	(Text and data)
poly	pin	66:16	(Text and data)
diff	pin	65:16	(Text and data)
nwell	pin	64:16	(Text type)
pad	pin	76:16	(Text and data)
pwell	pin	122:16	(Text and data)
pwelliso	pin	44:16	(Text and data)

nwell	pin	64:0	(Text type)
poly	pin	66:0	(Text type)
li1	pin	67:0	(Text type)
met1	pin	68:0	(Text type)
met2	pin	69:0	(Text type)
met3	pin	70:0	(Text type)
met4	pin	71:0	(Text type)
met5	pin	72:0	(Text type)
pad	pin	76:0	(Text type)
pwell	pin	122:0	(Text type)

diff	cut	65:14
poly	cut	66:14
li1	cut	67:14
met1	cut	68:14
met2	cut	69:14
met3	cut	70:14
met4	cut	71:14
met5	cut	72:14
pwell	cut

met5	probe	72:25
met4	probe	71:25
met3	probe	70:25
met2	probe	69:25
met1	probe	68:25
li1	probe	67:25
poly	probe	66:25

poly	short	66:15
li1	short	67:15
met1	short	68:15
met2	short	69:15
met3	short	70:15
met4	short	71:15
met5	short	72:15

Mask level data

cncm	mask	17:0	N-core implant mask
crpm	mask	96:0	Resistor Protect mask
cpdm	mask	37:0	Pad mask
cnsm	mask	22:0	Nitride seal mask
cmm5	mask	59:0	Metal 5 mask
cviam4	mask	58:0	Via 4 mask
cmm4	mask	51:0	Metal 4 mask
cviam3	mask	50:0	Via 3 mask
cmm3	mask	34:0	Metal 3 mask
cviam2	mask	44:0	Via 2 mask
cmm2	mask	41:0	Metal 2 mask
cviam	mask	40:0	Via mask
cmm1	mask	36:0	Metal 1 mask
ctm1	mask	35:0	Contact mask
cli1m	mask	56:0	Local interconnect mask
clicm1	mask	43:0	Local interconnect contact mask
cpsdm	mask	32:0	P+ Implant mask
cnsdm	mask	30:0	N+ Implant mask
cldntm	mask	11:0	Lightly-doped N-tip implant mask
cnpc	mask	49:0	Nitride poly cut mask
chvntm	mask	39:0	High voltage N-tip implant mask
cntm	mask	27:0	N-tip implant mask
cp1m	mask	28:0	Poly 1 mask
clvom	mask	46:0	Low Voltage oxide mask
conom	mask	88:0	ONO Mask
ctunm	mask	20:0	Tunnel mask
chvtrm	mask	98:0	HLow VT PCh Radio mask
chvtpm	mask	97:0	High Vt Pch mask
clvtnm	mask	25:0	Low Vt Nch mask
cnwm	mask	21:0	Nwell mask
cdnm	mask	48:0	Deep nwell mask
cfom	mask	23:0	Field oxide mask

cfom	drawing	22:20
clvtnm	drawing	25:44
chvtpm	drawing	88:44
conom	drawing	87:44
clvom	drawing	45:20
cntm	drawing	26:20
chvntm	drawing	38:20
cnpc	drawing	44:20
cnsdm	drawing	29:20
cpsdm	drawing	31:20
cli1m	drawing	115:44
cviam3	drawing	112:20
cviam4	drawing	117:20
cncm	drawing	96:44

cntm	mask add	26:21
clvtnm	mask add	25:43
chvtpm	mask add	97:43
cli1m	mask add	115:43
clicm1	mask add	106:43
cpsdm	mask add	31:21
cnsdm	mask add	29:21
cp1m	mask add	33:43
cfom	mask add	22:21

cntm	mask drop	26:22
clvtnm	mask drop	25:42
chvtpm	mask drop	97:42
cli1m	mask drop	115:42
clicm1	mask drop	106:42
cpsdm	mask drop	31:22
cnsdm	mask drop	29:22
cp1m	mask drop	33:42
cfom	mask drop	22:22

cmm4	waffle drop	112:4
cmm3	waffle drop	107:24
cmm2	waffle drop	105:52
cmm1	waffle drop	62:24
cp1m	waffle drop	33:24
cfom	waffle drop	22:24
cmm5	waffle drop	117:4